## Slide 2: Computer Organization

## Slide 3: Computer Organization
It deals with the hardware components of a computer system such as the input/output devices, CPU and memory devices
Notes: Computer systems have four parts—Hardware—Software—Data--User
Hardware---Mechanical devices in the computer---Anything that can be touched
Software---Tell the computer what to do---Also called a program---Thousands of programs exist
Data---Pieces of information---Computer organize and present data
Users---People operating the computer---Most important part---Tell the computer what to do

## Slide 4: Parts of the Computer System
Hardware
  Mechanical devices in the computer
  Anything that can be touched
Software
  Tell the computer what to do
  Also called a program
  Thousands of programs exist

## Slide 5: Parts of the Computer System
Data
  Pieces of information
  Computer organize and present data
Users
  People operating the computer
  Most important part
  Tell the computer what to do

## Slide 6: 1.Hardware

## Slide 7: Essential Computer Hardware
CRT Display
Keyboard
Mouse
“The Box”
Computers use the same basic hardware
Hardware categorized into four types
Notes: Computers use the same basic hardware
Hardware categorized into four types
CRT (cathode ray tube) monitors
LCD (liquid crystal display) monitors
LED (light-emitting diodes) monitors

## Slide 8: Inside the box
Motherboard
CPU
(Central Processing Unit)
(RAM)
HDD
(Hard Disk Drive)

## Slide 9: Mother-board
It holds together many of the crucial components of a computer
Parts of a Motherboard
  A CPU socket
  A power connector
  A Slots for RAM
  A second chip controls the input and output (I/O) functions
  A Slots for one or more hard drives
  A read-only memory (ROM) chip
  A slot for a video or graphics card
Notes: A motherboard is one of the most essential parts of a computer system. It holds together many of the crucial components of a computer, including the central processing unit (CPU), memory and connectors for input and output device

## Slide 10: Central Processing Unit
It is the brain of a computer system.
Carries out instructions from the program.
Performs the basic arithmetical, logical, and input/output operations.
!!Remember that this is all about speed.
Components
ALU
CU
Cache
Notes: ALU—Calculations occure
Control Unit----manages and coordinates the operations of all other components--
Cache---, which serves as high-speed memory where instructions can be copied to and retrieved

## Slide 11: Arithmetic Logic Unit- ALU
An arithmetic logic unit (ALU) is a digital circuit used to perform arithmetic and logic operations.
The control unit moves the data between these registers, the ALU, and memory.
Notes: It represents the fundamental building block of the central processing unit (CPU).
Modern CPUs contain very powerful and complex ALUs. In addition modern CPUs contain a control unit (CU).
Most of the operations of a CPU are performed by one or more ALUs, which load data from input registers.
A register is a small amount of storage available as part of a CPU.
The control unit tells the ALU what operation to perform on that data, and the ALU stores the result in an output register.

## Slide 12: How an ALU Works
There are also circuits for multiplying, for comparing two numbers, etc.
Transistor switches are used to manipulate binary numbers
  An open transistor represents a 0.
  A closed transistor represents a 1.
Arithmetic operations
addition
Subtraction
Logic operations
NOT
AND
Multiplication
division
OR
comparisons of values such as
Notes: ALU performs basic arithmetic and logic operations
All information in a computer is stored and manipulated in the form of binary numbers, i.e. 0 and 1.
Transistor switches are used to manipulate binary numbers since there are only two possible states of a switch: open or closed. An open transistor, through which there is no current, represents a 0. A closed transistor, through which there is a current, represents a 1.

## Slide 13: Control Unit (CU)
One of the two basic components of CPU
Acts as the central nervous system of a computer system
Selects and interprets program instructions, and coordinates execution
Fetch  decode  execute  write back  fetch
Has some special purpose registers and a decoder to perform these activities
!!The control unit moves the data between these registers, the ALU, and memory.

## Slide 14: RAM&ROM
  Stores data or programs
  Random Access Memory (RAM)
    Volatile
    Stores current data and programs
    More RAM results in a faster system
    2 to 8 GB
  Read Only Memory (ROM)
    Permanent storage of programs
    Holds the computer boot directions
Notes: Intel, the manufacturer of popular CPUs, originally made RAM for mainframe and minicomputers. Today Kingston is a leading RAM manufacturer.
A RAM device makes it possible to access data in random order, which makes it very fast to find a specific piece of information.
RAM is considered volatile memory, which means that the stored information is lost when there is no power.

## Slide 15: Storage devices
  Hold data and programs permanently
  Different from RAM
  Magnetic storage
    Floppy and hard drive
    Uses a magnet to access data
  Optical storage
    CD and DVD drives
    Uses a laser to access data
Notes: Each tiny bit of the disk carries a magnetic charge; the direction of that charge determines whether it represents a 1 or a 0. Optical storage, meanwhile, uses disks made of reflective material; how each bit reflects light–or doesn't reflect it–determines whether it's a 1 or a 0.
VIDEO OF THE DAY

## Slide 16: I/O devices
Allows the user to interact
  Some devices are input and output
    Touch screens
Input Devices
Any peripheral (piece of computer hardware equipment) used to provide data and control signals to a computer.
Allows the user to put data into the computer.
Output Devices
Any peripheral that deliver data
Computer hardware equipment used to communicate the results of data processing carried out by a computer to the outside world.
Notes: Examples of Input Device—Keyboard—Mouse--Touchscreen--Graphic tablet---Microphone---Scanner
Examples of Output Device--Monitor--Printer--Speakers--Projector

## Slide 17: Software

## Slide 18: Software
Tells the computer what to do
Reason people purchase computers
Two types
  System software
  Application software
System software
  Most important software
  Operating system
    Windows XP
  Network operating system (OS)
    Windows Server 2003
  Utility
    Symantec Antivirus
Application software
  Accomplishes a specific task
  Most common type of software
    MS Word
  Covers most common uses of computers
Software
System software
Operating system
Utility software
Device drivers
Application software
Custom built
Packaged software
Notes: System software--Most important software---Operating system---Windows XP---Network operating system (OS)---Windows Server 2003---Utility---Symantec Antivirus
Application software---Accomplishes a specific task---Most common type of software---MS Word---Covers most common uses of computers

## Slide 19: Basic organization of computer system

## Slide 20: Basic organization of computer system
Notes: 1. The Central Processing Unit (CPU)
2. The Main Memory Unit (RAM)
3. The Input / Output Device

## Slide 21: Von Neumann Basic Structure
Let’s consider them in detail.
Arithmetic and Logic Unit (ALU)
  The arithmetic logic unit is that part of the CPU that handles all the calculations the CPU may need, e.g. Addition, Subtraction, Comparisons.
  It performs Logical Operations, Bit Shifting Operations, and Arithmetic Operation.
Control Unit
  A control unit (CU) handles all processor control signals. It directs all input and output flow, fetches code for instructions and controlling how data moves around the system.

## Slide 23: PROCESSOR AND MEMORY

## Slide 24: Basic Processor & Memory Architecture of a Computer System
Main Memory (RAM)
Cache Memory
Input/Output
register
Decode r Program
control register
Instruction register
Memory address register
Memory buffer register
Accumulato
r register
General-
purpose register
General- purpose register
General-purpose register
General- purpose register
Control Unit
I/ O
D E V I C E S
ROM PROM Flash
Ref Page

## Slide 25: Computer BUS
Bus:
Inside computers, there are many internal components. For these components to communicate with each other they make use of wires that are known as a ‘bus’ .
A bus is a common pathway through which information flows from one computer component to another. This pathway is used for communication purpose and it is established between two or more computer components.
Types of Bus:
Data bus is used for transfer of data between subunits
Address bus is used to transmit location information between units such as where the data is going or coming from.
Control bus control working of other components. It is used to provide information as to how data is being sent.

## Slide 26
Notes: Control bus specifies the type of operation that is to be performed (read write commands, bus request/grant etc) travel on control bus
E.g. acknowledgement signals travel on control bus

## Slide 27
Notes: Carries address signal to read or write data to memory

## Slide 29: Instruction Set
The complete set of all the instructions in machine code that can be recognized and executed by a central processing unit.
CPU has built-in ability to execute a set of machine instructions, called its instruction set
Most CPUs have 200 or more instructions (such as add, subtract, compare, etc.) in their instruction set
CPUs made by different manufacturers have different instruction sets
Manufacturers tend to group their CPUs into “families” having similar instruction sets
New CPU whose instruction set includes instruction set of its predecessor CPU is said to be backward compatible with its predecessor

## Slide 30: Registers
Special memory units, called registers, are used to hold information on a temporary basis as the instructions are interpreted and executed by the CPU
Registers are part of the CPU (not main memory) of a computer and is super fast memory.
The length of a register, sometimes called its word size, equals the number of bits it can store
With all other parameters being the same, a CPU with 32-bit registers can process data twice larger than one with 16-bit registers

## Slide 31: Functions of Commonly Used Registers
Sr. No. | Name of Register | Function
1 | Memory Address (MAR) | Holds address of the active memory location
2 | Memory Buffer (MBR) | Holds contents of the accessed (read/written) memory word
3 | Program Control (PC) | Holds address of the next instruction to be executed
4 | Accumulator (AC) | Holds data intermediate results, and the results
5 | Instruction (I) | Holds an instruction while it is being executed
6 | Input/Output (I/O) | Used to communicate with the I/O devices
Notes: A memory buffer register (MBR) is the register in a computer's processor, or central processing unit, CPU, that stores the data being transferred to and from the immediate access store.
Accumulator Register This Register is used for storing the Results those are produced by the System.

## Slide 32: CPU Registers
Accumulator: Stores the results of calculations made by ALU.
Program Counter (PC): Keeps track of the memory location of the next instructions to be dealt with. The PC then passes this next address to Memory Address Register (MAR).
Memory Address Register (MAR): Holds the address of the location in memory, which contains data, that is required by the current instruction being executed. simply MAR points to the memory location that contains data required.
Memory Data Register (MDR): It stores instructions fetched from memory or any data that is to be transferred to, and stored in, memory.
Current Instruction Register (CIR): Holds the instruction currently being executed or decoded.
Instruction Buffer Register (IBR): The instruction that is not to be executed immediately is placed in the instruction buffer register IBR.

## Slide 33: CPU Registers

## Slide 34: Fetch decode execute cycle
Fetch :
Get an instruction from main memory
Decode:
Translate it into computer command
Execute:
Actual processing of command
Store/Write back:
Write result to memory.

## Slide 35: Fetch decode execute cycle

## Slide 36: The Fetch/Execute Cycle
“Instruction Execution Engine”…a machine that cycles through a series of operations
Series is called: Fetch/Execute Cycle
  Get the next instruction
  Figure out what to do
  Gathering the data needed to do it
  Do it
  Save the result, and
  Repeat (billions of times/second)!

## Slide 37: A Five-Step Cycle
These operations are repeated in a never-ending sequence
A five-step cycle:
  Instruction Fetch (IF)
  Instruction Decode (ID)
  Data Fetch (DF) / Operand Fetch (OF)
  Instruction Execution (EX)
  Result Return (RR) / Store (ST)

## Slide 38: A Five-Step Cycle

## Slide 39: ADD 800, 428, 884

## Slide 40: Instruction Fetch (IF)
Execution begins by moving the instruction at the address given by the (PC 2200) from memory to the control unit
Once instruction is fetched, the PC can be changed for fetching the next instruction

## Slide 41: IF
Notes: Execution begins by moving the instruction at the address given by the PC (PC 2200) from memory to the control unit
Once instruction is fetched, the PC can be readied for fetching the next instruction

## Slide 42: Instruction Decode (ID)
ALU is set up for the operation
Decoder finds the memory address of the instruction's data (source operands)
  Most instructions operate on two data values stored in memory (like ADD), so most instructions have addresses for two source operands
  These addresses are passed to the circuit that fetches them from memory during the next step
  Decoder finds the destination address for the Result Return step and places the address in the RR circuit
  Decoder determines what operation the ALU will perform (ADD), and sets up the ALU

## Slide 43: ID

## Slide 44: Data Fetch (DF)
The data values to be operated on are retrieved from memory
Bits at specified memory locations are copied into locations in the ALU circuitry
Data values remain in memory (they are not destroyed)

## Slide 45: DF

## Slide 46: Instruction Execution (EX)
For this ADD instruction, the addition circuit adds the two source operands together to produce their sum
Sum is held in the ALU circuitry
This is the actual computation

## Slide 47: EX

## Slide 48: Return Result (RR)
RR returns the result of EX to the memory location specified by the destination address.
Once the result is stored, the cycle begins again

## Slide 49: RR

## Slide 50: Cycling the Fetch/Execute Cycle
ADD is representative of the complexity of computer instructions…some are slightly simpler, some slightly more complex
Computers achieve success at what they can do with speed.
They show their impressive capabilities by executing many simple instructions per second

## Slide 51: Many, Many Simple Operations
Computers “know” very few instructions
The decoder hardware in the controller recognizes, and the ALU performs, only about 100 different instructions (with a lot of duplication)
There are only about 20 different kinds of operations.
Everything that computers do must be reduced to some combination of these primitive, hardwired instructions

## Slide 52: Processor and Memory

## Slide 53: Memory
Memory stores both the program while it is running and the data on which the program operates
Properties of memory:
  Discrete locations
    Memory is organized as a sequence of discrete locations
    In modern memory, each location is composed of 1 byte (8 bits)

## Slide 54: Memory
Addresses
  Every memory location has an address, whole numbers starting at 0
Values
  Memory locations record or store values
Finite capacity
  Memory locations have a finite capacity (limited size),
  Data may not “fit” in the memory location

## Slide 55: Byte-Size Memory Location
Common visualization of computer memory
Discrete locations are shown as boxes holding 1-byte each
Address of location is displayed above the box and the contents of location is shown in the box

## Slide 56: Byte-Size Memory Location
That 1-byte memory location can store one ASCII character or a number less than 256
Blocks of four bytes are used as a unit so often that they are called memory words.

## Slide 57: RAM
Computer memory is called random access memory (RAM)
  “Random access” is out-of-date and simply means that the computer can refer to the memory locations in any order
RAM is measured in megabytes (MB) or gigabytes (GB)
Lots of memory is need to handle the space required of programs and data

## Slide 58: Storage Evaluation Criteria
Property | Desirable | Primary storage | Secondary storage
Storage capacity | Large storage capacity | Small | Large
Access Time | Fast access time | Fast | Slow
Cost per bit of storage | Lower cost per bit | High | Low
Volatility | Non-volatile | Volatile | Non-volatile
Access | Random access | Random access | Pseudo-random access or sequential access

## Slide 59: Main Memory Organization
Addresses of a memory
The words of a memory
(total N words)
0
1
2
3
4
5
N-2
N-1
Bit 1 Bit 2
Ref Page
Each word contains the same number of bits = word length

## Slide 60: Fixed Word-length Memory
Storage space is always allocated in multiples of word-length
Faster in speed of calculation than variable word-length memory
Normally used in large scientific computers for gaining speed of calculation
0501
0502
0503
 |  | L | A | H | O | R | E
 |  |  | G | A | M | E | S
Address Numbers

## Slide 61: Variable Word-length Memory
L
A
H
O
R
E
0025
0026
0027
0028
0029
0030
0031
4096
G
A
M
E
S
0051
0052
0053
0054
0055
0056
4096
Each memory location can store only a single character
Slower in speed of calculation than fixed world-length memory
Used in small business computers for optimizing the use of storage space
Ref Page
Note: With memory becoming cheaper and larger day-by-day, most modern computers employ fixed-word-length memory organization
Character addressable
Address Numbers
Address Numbers

## Slide 62: Memory Capacity
Memory capacity of a computer is equal to the number of bytes that can be stored in its primary storage
Its units are:
Kilobytes (KB) : 1024 (210) bytes
Megabytes (MB) : 1,048,576 (220) bytes
Gigabytes (GB) : 1,073,741824 (230) bytes

## Slide 63: Control unit-CU
The control unit of a computer is where the Fetch/Execute Cycle occurs
Its circuitry fetches an instruction from memory and performs the other operations of the Fetch/Execute Cycle on it
A typical machine instruction has the form ADD 4000, 2000, 2080

## Slide 64: Task
ADD 4000, 2000, 2080
  Looks like those three numbers should be added together
  What it really means is that whatever numbers are stored in memory locations 2000 and 2080 be added together, and the result be stored in location 4000

## Slide 65: task

## Slide 66: Storage Hierarchy
Capacity and access are inversely proportional to each other

## Slide 67: The Program Counter (PC)
How does the computer determine which instruction it should execute next?
Address of the Next Instruction
  The instruction is stored in memory and the computer has its address
  Computers use the address (known as the program counter or PC) to keep track of the next instruction

## Slide 68: The Program Counter
The computer gets ready to process the next instruction
It assumes that the next instruction is the next instruction in sequence
Because instructions use 4 bytes of memory, the next instruction must be at the memory address PC + 4 or 4 bytes further along the sequence

## Slide 69: The Computer Clock
Computers are instruction execution engines.
Since the computer does one instruction per cycle in principle, the speed of a computer depends on the number of Fetch/Execute Cycles it completes per second.

## Slide 70: The Computer Clock
The rate of the Fetch/Execute Cycle is determined by the computer’s clock, and it is measured in megahertz, or millions (mega) of cycles per second (hertz).
A 1,000 MHz clock ticks a billion (in American English) times per second, which is one gigahertz (1 GHz)

## Slide 71: Standard Prefixes

## Slide 72: One Cycle per Clock Tick
A computer with a 1 GHz clock has one billionth of a second—one nanosecond—between clock ticks to run the Fetch/Execute Cycle.
In that amount of time, light travels about one foot (~30 cm).
Modern computers try to start an instruction on each clock tick.

## Slide 73: Computer’s View of Software
A program “sees” software as a long sequence of 4-byte groups of bits (0's and 1’s)
This binary object file can be hundreds of thousands to millions of words long

## Slide 74: Computer’s View of Software
Once installed, the computer runs the software by:
  copying the binary instructions into the RAM
  interpreting them using the Fetch/Execute Cycle.
It does whatever the instructions tell it to do

## Slide 75: Processor Speed
Computer has a built-in system clock that emits millions of regularly spaced electric pulses per second (known as clock cycles)
It takes one cycle to perform a basic operation, such as moving a byte of data from one memory location to another
Normally, several clock cycles are required to fetch, decode, and execute a single program instruction
Hence, shorter the clock cycle, faster the processor
Clock speed (number of clock cycles per second) is measured in Megahertz (106 cycles/sec) or Gigahertz (109 cycles/sec)

## Slide 76: ACTIVITY
Develop fetch and execute cycle with instructions, manipulating registers memory and change the state of memory.
ADD X, Y, Z
X=27
Y=56
Z=60
!! Convert XYZ in to 8bit address

## Slide 77: Recommended
https://www.futurelearn.com/courses/how-computers-work/0/steps/49284