## Slide 1: CS 3006 Parallel and Distributed Computing Lecture 3
Danyal Farhat
FAST School of Computing
NUCES Lahore

## Slide 2: Flynn’s Classical Taxonomy and Processor to Memory Connection Strategies

## Slide 3: Outline
Flynn’s Classical Taxonomy
Processor Organizations
SISD
SISD – Multithreading
  Implicit Multithreading
  Explicit Multithreading
Intel’s Hyper Threading Technology
SIMD
  SIMD - Examples

## Slide 4: Outline
MISD
MIMD
MIMD - Shared Memory
  Uniform Memory Access (UMA)
  Non-Uniform Memory Access (NUMA)
MIMD - Distributed Memory
Shared Memory Interconnection Network
Summary

## Slide 5: Flynn’s Classical Taxonomy
Hardware architecture classifications – Flynn, Feng, Handler
Most widely used parallel computer classifications
Differentiates multiprocessor computers according to the dimensions of instruction and data
  Instruction stream: Sequence of instructions from memory to control unit
  Data stream: Sequence of data from memory to control unit
SISD: Single Instruction stream, Single Data stream
SIMD: Single Instruction stream, Multiple Data stream
MISD: Multiple Instruction stream, Single Data stream
MIMD: Multiple Instruction stream, Multiple Data stream

## Slide 6: Processor Organizations

## Slide 7: SISD
A serial (non-parallel computer)
Single instruction: one instruction per cycle
Single data: only one data stream per cycle
Easy and deterministic execution
Example:
Single CPU workstations
Most workstations from HP, IBM and SGI are SISD machines

## Slide 8: SISD (Cont.)
Performance of a processor can be measured with:
MIPS Rate = f x IPC
  Million instructions per second (MIPS) is an approximate measure of a computer's raw processing power
  f (clock frequency of processor); IPC (instructions per cycle)
How to increase performance of uniprocessor?
Using Multithreading
Increasing clock frequency
Increasing number of instructions completed during a processor cycle (multiple pipelines in a superscalar architecture and/or out of order execution)

## Slide 9: SISD – Multithreading
Run multiple threads on the same core concurrently
Context switch implemented in hardware
Minimum hardware support: replicate architectural state
  All running threads must have their own context
  Multiple register sets in the core
  Multiple state registers
    Program Counter (PC)
    Memory Address Register (MAR)
    Accumulator Register (ACC)

## Slide 10: SISD – Multithreading (Cont.)
Implicit Multithreading
concurrent execution of multiple threads extracted from a single sequential program
Managed by processor hardware
Improve individual application performance
Explicit Multithreading
concurrent execution of instructions from different explicit threads, either by interleaving instructions from different threads or by parallel execution on parallel pipelines

## Slide 11: SISD-Explicit Multithreading
Four approaches for explicit multithreading
  Interleaved multithreading (fine-grained): fetch instructions from different threads in consecutive cycles. In case of few active threads, performance degrades
  Blocked multithreading (coarse-grained): events like cache miss produce switch
  Simultaneous multithreading (SMT): execution units of a superscalar processor receive instructions from multiple threads
  Chip multiprocessing: e.g. dual core (not SISD)
Architectures like IA-64 Very Long Instruction Word (VLIW) allow multiple instructions (to be executed in parallel) in a single word

## Slide 12: Intel’s Hyper Threading Technology
A single physical processor appears as two logical processors by applying two-threaded SMT approach
  Example: Intel Pentium 4 in 2002
Each logical processor maintains a complete set of architecture state (general-purpose registers, control registers,…)
Logical processors share nearly all other resources such as caches, execution units, branch predictors, control logic and buses

## Slide 13: Intel’s Hyper Threading Technology (Cont.)
Partitioned resources are recombined when only one thread is active
Add less than 5% to the relative chip size
Improve performance by 16% to 28%

## Slide 14: SIMD
Homogeneous processing units / processing elements (PEs)
Single instruction: All processor units execute the same instruction at any given time
Multiple data: Each processing unit can operate on different data set
  Example: Add A and B, C and D, X and Z

## Slide 15: SIMD (Cont.)
Each processing element has an associated data memory
  So that each instruction is executed on a different set of data by the different processors
Used by vector and array processors
  Suitable for vector and matrix calculations
Vector processors act on array of similar data (only when executing in vector mode) and in this case they are several times faster than when executing in scalar mode
  Example: NEC SX-8 processors run at 2 GHz for vectors and 1 GHz for scalar operations

## Slide 16: SIMD - Examples
A good example is the processing of pixels on screen
A sequential processor would examine each pixel one at a time and apply the processing instruction
An array or vector processor can process all the elements of an array simultaneously
Game consoles and graphic cards make heavy use of such processors to shift those pixels
Such designs are usually dedicated to a particular application and not commonly marketed for general purpose computing

## Slide 17: SIMD-Examples (Cont.) – Super Mario

## Slide 18: MISD
A single data stream is transmitted to a set of processors, each of which executes a different instruction sequence
Each processing unit operates on the data independently via independent instruction stream
This structure is not commercially implemented
Example: Multiple cryptography algorithms attempting to crack a coded message

## Slide 19: MIMD
Multiple instruction: Every processor may execute a different instruction stream
Multiple data: Every processor may work with a different data stream
Examples:
Most of the current supercomputers
Grid computers
Networked parallel computers
Symmetric Multiprocessors (SMP) computers

## Slide 20: MIMD (Cont.)
MIMD systems are mainly:
Shared Memory (SM) Systems:
Multiple CPUs share same address space
  There is only one memory
Distributed Memory (DM) Systems:
Each CPU has its own associated memory
CPUs are connected by some network (clusters)

## Slide 21: MIMD - Shared Memory
All processors have access to all memory as a global address space

## Slide 22: Uniform Memory Access (UMA)
From all processing units to the shared memory, the data access time is constant.
Mostly represented by Symmetric Multiprocessor (SMP) machines.

## Slide 23: Non-Uniform Memory Access (NUMA)
From all processing units to the shared memory, the data access time is not constant.

## Slide 24: Shared Memory Interconnection Network
Main problem is how to do interconnections of the CPUs to each other and to the memory
There are three main network topologies available:
Crossbar (n x n connections - datapath without sharing)
-network(n log2 n connections - log2 n switching stages and shared on a path)
Central databus (O(1) connections - n shared)

## Slide 25: Shared Memory Interconnection Network (Cont.)

## Slide 26: Summary
Flynn’s Classical Taxonomy
  Differentiates multiprocessor computers on the basis of dimensions of instruction and data
Processor Organizations
  SISD - Used in uniprocessor computers
  SIMD - Used in vector or array processor computers
  MISD - Not commercially implemented
  MIMD - Used in supercomputers, grid computers etc.

## Slide 27: Summary (Cont.)
SISD
  Easy and deterministic but with limited performance
  SISD processor performance - MIPS Rate = f x IPC
  How to increase performance of uniprocessor?
SISD – Multithreading
  Implicit Multithreading - Implemented at compiler or OS kernel level
  Explicit Multithreading - Defined be the programmer
    Interleaved multithreading
    Blocked multithreading
    Simultaneous multithreading

## Slide 28: Summary (Cont.)
Intel’s Hyper Threading Technology
  Single physical processor appears as two logical processors by applying two-threaded SMT approach (Used in Pentium 4 PCs - 2002)
SIMD
  Homogeneous processing units (vector or array processors)
  Execution of single instruction on multiple data sets using single control unit
  Associated data memory for each processing element
SIMD – Examples
  Processing of pixels, online gaming servers, matrix based calculations etc.

## Slide 29: Summary (Cont.)
MISD
  Single data stream transmitted to a set of processors, each of which executes a different instruction sequence
  Commercially not implemented
  Example: Multiple cryptography algorithms attempting to crack a coded message
MIMD
  Supercomputers, Grid computers, Networked parallel computers etc.

## Slide 30: Summary (Cont.)
MIMD - Shared Memory - CPUs share same address space
  Uniform Memory Access (UMA) - Constant data access time
  Non-Uniform Memory Access (NUMA) - Non-Constant data access time
MIMD - Distributed Memory
  CPUs connected via network and have their own associated memory
Shared Memory Interconnection Network
  Crossbar - n x n connections, no path sharing
  Omega Network - n log n connections, shared path
  Bus - O (1) connections, shared path

## Slide 31: Questions?