## Slide 1: CS 3006 Parallel and Distributed Computing Lecture 8
Danyal Farhat
FAST School of Computing
NUCES Lahore

## Slide 2: Miscellaneous Topics

## Slide 3: Outline
Motivating Parallelism
  The Memory / Disk Speed Argument
  The Data Communication Argument
Types of Parallelism
  Data Parallelism
  Functional Parallelism
  Pipelining
Multi-Processor vs. Multi-Computer
Cluster vs. Network of Workstations

## Slide 4: Outline (Cont.)
Cache Coherence
Snooping
Branch Prediction
Architecture of an Ideal Parallel Computer - PRAM
PRAM Classes
PRAM Arbitration Protocols
Physical Complexity of an Ideal Parallel Computer
Communication Costs in Parallel Machines

## Slide 5: Outline (Cont.)
Message Passing Costs in Parallel Computers
  Startup time, Per-hop time, Per-word transfer time
  Store-and-Forward Routing, Packet Routing, Cut-Through Routing
  Simplified Cost Model for Communicating Messages
Summary
Additional Resources

## Slide 6: Motivating Parallelism
The Memory / Disk Speed Argument
While clock rates of high-end processors have increased at roughly 40% per year over the past decade, DRAM access times have only improved at the rate of roughly 10% per year over this interval
This mismatch in speeds causes significant performance bottlenecks
Parallel platforms provide increased bandwidth to the memory system

## Slide 7: Motivating Parallelism (Cont.)
The Memory / Disk Speed Argument
Parallel platforms also provide higher aggregate caches
Some of the fastest growing applications of parallel computing utilize not their raw computational speed, rather their ability to pump data to memory and disk faster
  CPU is fast but memory isn’t, which is a mismatch in context of parallel programming
  Solution: Parallel platform (increased bandwidth to memory) and combination or collection of caches

## Slide 8: Motivating Parallelism (Cont.)
The Data Communication Argument
As the network evolves, the vision of the Internet as one large computing platform has emerged.
In many applications like databases and data mining problems, the volume of data is such that they cannot be moved.
Any analyses on this data must be performed over the network using parallel techniques

## Slide 9: Types of Parallelism
Data Parallelism
When there are independent tasks applying the same operation to different elements of a data set
Example code
  for i=0 to 99 do
  a[ i ] = b[ i ] + c [ i ]
  Endfor
Here same operation addition is being performed on first 100 elements of ‘b’ and ‘c’ arrays
All 100 iterations of the loop could be executed simultaneously

## Slide 10: Types of Parallelism (Cont.)
Functional Parallelism
When there are independent tasks applying different operations to different data elements
Example code
a=2
b=3
m= (a+b) / 2
s= (𝒂 x a + 𝒃 x b) / 2
v= s - 𝒎^𝟐
Here third and fourth statements could be performed concurrently

## Slide 11: Types of Parallelism (Cont.)
Pipelining
Usually used for the problems where single instance of the problem can not be parallelized
The output of one stage is input of the other stage
Dividing whole computation of each instance into multiple stages provided that there are multiple instances of the problem

## Slide 12: Types of Parallelism (Cont.)
Pipelining (Cont.)
An effective method of attaining parallelism on the uniprocessor architectures
Depends on pipelining abilities of the processor
  Pentium 2 supports 12 stage pipelining
  Pentium 4 supports 20 stage pipelining at 2.0 GHz

## Slide 13: Types of Parallelism (Cont.)
Pipelining Example: Assembly line analogy

## Slide 14: Types of Parallelism (Cont.)
Pipelining Example: Assembly line analogy

## Slide 15: Types of Parallelism (Cont.)
Pipelining Example: Assembly line analogy

## Slide 16: Multi-Processor vs. Multi-Computer
Multi-Processor
Multiple CPUs with a shared memory
Same address on two different CPUs refers to the same memory location
Generally two categories
  Centralized Multi-processor
  Distributed Multi-processor

## Slide 17: Multi-Processor vs. Multi-Computer (Cont.)
Centralized Multi-Processor
Additional CPUs are attached to the system bus, and all the processors share the same primary memory
All the memory is at one place and has the same access time from every processor
Also known to as UMA (Uniform Memory Access) Multi-processor or SMP (Symmetrical Multi-processor)

## Slide 18: Multi-Processor vs. Multi-Computer (Cont.)
Distributed Multi-processor
Distributed collection of memories forms one logical address space
Again, the same address on different processors refers to the same memory location
Also known as Non-Uniform Memory Access (NUMA) architecture
Because, memory access time varies significantly, depending on the physical location of the referenced address

## Slide 19: Multi-Processor vs. Multi-Computer (Cont.)
Multi-Computer
Distributed memory, multi-CPU computer
Unlike NUMA architecture, a multicomputer has disjoint local address spaces
Each processor has direct access to their local memory only
Same address on different processors refers to two different physical memory locations
Processors interact with each other through passing messages

## Slide 20: Multi-Processor vs. Multi-Computer (Cont.)
Asymmetric Multi-Computers
A front-end computer that interacts with users and I/O devices
The back-end processors are dedicatedly used for “number crunching”
Front-end computer executes a full, multi-programmed OS and provides all functions needed for program development
The backends are reserved for executing parallel programs

## Slide 21: Multi-Processor vs. Multi-Computer (Cont.)
Symmetric Multi-Computers
Every computer executes same OS
Users may log into any of the computers
This enables multiple users to concurrently login, edit and compile their programs
All the nodes can participate in execution of a parallel program

## Slide 22: Cluster vs. Network of Workstations
Cluster
Usually a co-located collection of low-cost computers and switches, dedicated to running parallel jobs
All computer run the same version of operating system
Some of the computers may not have interfaces for the users to login
Commodity cluster uses high speed networks for communication such as fast Ethernet at 100Mbps etc.
Network of workstations
A dispersed collection of computers
Individual workstations may have different Operating systems and executable programs
Users have the power to login and power off their workstations
Ethernet speed for this network is usually slower.
  Typical in range of 10s Mbps

## Slide 23: Cache Coherence
When we are in a distributed environment, each CPU’s cache needs to be consistent (continuously needs to be updated for current values), which is known as cache coherence

## Slide 24: Snooping
Snoopy protocols achieve data consistency between the cache memory and the shared memory through a bus-based memory system
Write-invalidate and write-update policies are used for maintaining cache consistency

## Slide 25: Branch Prediction
Branch prediction is a technique used in CPU design that attempts to guess the outcome of a conditional operation and prepare for the most likely result
Issues in pipelining of branch prediction:
  If the prediction is true then the pipeline will not be flushed and no clock cycles will be lost
  If the prediction is false then the pipeline is flushed and starts over with the current instruction

## Slide 26: Physical Organization of Parallel Platforms
Architecture of an Ideal Parallel Computer
Parallel Random Access Machine (PRAM)
  An extension to ideal sequential model: Random Access Machine (RAM)
  PRAMs consist of p processors
  A global memory
    Unbounded size
    Uniformly accessible to all processors with same address space
  Processors share a common clock but may execute different instructions in each cycle
  Based on simultaneous memory access mechanisms, PRAM can further be classified

## Slide 27: Graphical Representation of PRAM

## Slide 28: Parallel Random Access Machine (PRAM)
PRAM has a set of similar type of processors
Processors communicate with each other using the shared memory
N processors can perform independent operations on N number of data in a given time, this might lead to simultaneous access of same memory location by different processors
  To solve the simultaneous access of same memory location problem we have PRAM classes

## Slide 29: PRAM Classes
PRAMs can be divided into four classes
Exclusive-Read, Exclusive-Write (EREW) PRAM
  No two processors can perform read/write operations concurrently
  Weakest PRAM model, provides minimum memory access concurrency
Concurrent-Read, Exclusive-Write (CREW) PRAM
  All processors can read concurrently but can’t write at same time
  Multiple write accesses to a memory location are serialized
Exclusive-Read, Concurrent-Write (ERCW) PRAM
  No two processors can perform read operations concurrently, but can write
Concurrent-Read, Concurrent-Write (CRCW) PRAM
  Most powerful PRAM model

## Slide 30: PRAM Arbitration Protocols
Concurrent reads do not create any semantic inconsistencies
But, What about concurrent write?
Need of an arbitration (mediation) mechanism to resolve concurrent write access

## Slide 31: PRAM Arbitration Protocols (Cont.)
Common
  Write only if all values that processors are attempting to write are identical
Arbitrary
  Write the data from a randomly selected processor and ignore the rest
Priority
  Follow a predetermined priority order
  Processor with highest priority succeeds and the rest fail
Sum
  Write the sum of the data items in all the write requests
  The sum-based write conflict resolution model can be extended for any of the associative operators, that is defined for data being written

## Slide 32: Physical Complexity of an Ideal Parallel Computer
Processors and memories are connected via switches
Since these switches must operate in O(1) time at the level of words, for a system of p processors and m words, the switch complexity is O(mp)
  Switches determine the memory word being accessed by each processor
  Switch is a device that opens or closes access to certain data bank or word
Clearly, for meaningful values of p and m, a true PRAM is not realizable

## Slide 33: Communication Costs in Parallel Machines
Along with idling (doing nothing) and contention (conflict e.g., resource allocation), communication is a major overhead in parallel programs
The communication cost is usually dependent on a number of features including the following:
  Programming model for communication
    Required pattern of the communication in the program
  Network topology
  Data handling and routing
  Associated network protocols
Usually, distributed systems suffer from major communication overheads

## Slide 34: Message Passing Costs in Parallel Computers
The total time to transfer a message over a network comprises of the following:
Startup time (ts): Time spent at sending and receiving nodes (preparing the message [adding headers, trailers, and parity information] , executing the routing algorithm, establishing interface between node and router, etc.)

## Slide 35: Message Passing Costs in Parallel Computers (Cont)
Per-hop time (th): This time is a function of number of hops (steps) and includes factors such as switch latencies, network delays, etc.
  Also known as node latency
  Also accounts for the latency to take decision of choosing next channel to which this message shall be forwarded
Per-word transfer time (tw): This time includes all overheads that are determined by the length of the message. This includes bandwidh of links, and buffering overheads, etc.
  If channel bandwidth is r words/s then each word take tw= 1/r to traverse the link

## Slide 36: Message Passing Costs in Parallel Computers (Cont)
Store-and-Forward Routing
A message traversing multiple hops is completely received at intermediate hop before being forwarded to next hop
The total communication cost for a message of size m words to traverse l communication links is
In most platforms, th is small and the above expression can be approximated by
  Cost of header transfer at each hop (step) th ts is startup time
  mtw is cost of transferring m words over the link

## Slide 37: Message Passing Costs in Parallel Computers (Cont)
Packet Routing
Store-and-forward makes poor use of communication resources
Packet routing breaks messages into packets and pipelines them through the network
Since packets may take different paths, each packet must carry routing information, error checking, sequencing, and other related header information
  Error checking (parity information), sequencing (order number)
  Related headers: layers headers, addressing headers
The total communication time for packet routing is approximated by:
Here factor tw also accounts for overheads in packet headers

## Slide 38: Message Passing Costs in Parallel Computers (Cont)
Cut-Through Routing
Takes the concept of packet routing to an extreme by further dividing messages into basic units called flits or flow control digits
Since flits are typically small, the header information must be minimized
This is done by forcing all flits to take the same path, in sequence
A tracer message first programs all intermediate routers. All flits then take the same route

## Slide 39: Message Passing Costs in Parallel Computers (Cont)
Cut-Through Routing (Cont.)
Error checks are performed on entire message, as opposed to flits
No sequence numbers are needed
  Sequencing information is not needed as all the packets are following same path which ensures in-order delivery
The total communication time for cut-through routing is approximated by:
This is identical to packet routing, however, tw is typically much smaller
  Header of the message takes l* th to reach the destination and entire message arrives in time m tw after the message header

## Slide 40: Message Passing Costs in Parallel Computers (Cont.)
(a) through a store-and-forward communication network
b) and (c) extending the concept to cut-through routing
Shaded regions here represent the time where message is in transit (travel)
The startup time associated with this message transfer is assumed to be zero

## Slide 41: Message Passing Costs in Parallel Computers (Cont)
Simplified Cost Model for Communicating Messages
The cost of communicating a message between two nodes l hops away using cut-through routing is given by:
In this expression, th is typically smaller than ts and tw. For this reason, the second term in the RHS does not show, particularly, when m is large
For these reasons, we can approximate the cost of message transfer by:
  For communication using flits, start-up time dominates the node latencies

## Slide 42: Message Passing Costs in Parallel Computers (Cont)
Simplified Cost Model for Communicating Messages (Cont.)
It is important to note that the original expression for communication time is valid for only uncongested networks
Different communication patterns congest different networks to varying extents
It is important to understand and account for this in the communication time accordingly

## Slide 43: Summary
Motivating Parallelism
  The Memory / Disk Speed Argument
    Speed mismatch between processor and DRAM can be reduced using parallel platforms and aggregated caches
  The Data Communication Argument
    Analyses on large scale data can be performed over the network using parallel techniques

## Slide 44: Summary (Cont.)
Types of Parallelism
  Data Parallelism
    Independent tasks applying the same operation to different elements of a data set
  Functional Parallelism
    Independent tasks applying different operations to different data elements
  Pipelining
    Effective method of attaining parallelism on the uniprocessor architectures

## Slide 45: Summary (Cont.)
Multi-Processor vs. Multi-Computer
  Multi-Processor - Multiple CPUs with a shared memory
    Centralized Multi-Processor - All the memory is at one place and has Uniform Memory Access (UMA) architecture
    Distributed Multi-processor - Distributed collection of memories forms one logical address space. Use Non-Uniform Memory Access (NUMA) architecture
  Multi-Computer - Each processor has disjoint memory
    Asymmetric Multi-Computers
      A front-end computer interacts with users and I/O devices
      The back-end processors are dedicated for processing
    Symmetric Multi-Computers
      Every computer executes same OS
      This enables multiple users to concurrently login, edit and compile their programs

## Slide 46: Summary (Cont.)
Cluster vs. Network of Workstations
  Cluster - Co-located collection of computer with same version of OS
  Network of Workstations - Dispersed collection of computers with different versions of OS
Cache Coherence
  Cache continuously needs to be updated for current values
Snooping
  Snoopy protocols achieve data consistency between cache and memory through a bus based memory system

## Slide 47: Summary (Cont.)
Branch Prediction
  Used in CPU design to guess the outcome of a conditional operation and prepare for the most likely result
Architecture of an Ideal Parallel Computer – PRAM
  Extension to ideal sequential model: Random Access Machine (RAM)
  Consist of p processors
  Global memory (Unbounded size, Uniformly accessible to all processors with same address space)

## Slide 48: Summary (Cont.)
PRAM Classes
  Exclusive-Read, Exclusive-Write (EREW) PRAM
  Concurrent-Read, Exclusive-Write (CREW) PRAM
  Exclusive-Read, Concurrent-Write (ERCW) PRAM
  Concurrent-Read, Concurrent-Write (CRCW) PRAM
PRAM Arbitration Protocols
  Concurrent writes do create semantic inconsistencies
  We need an arbitration mechanism to resolve concurrent write access
  Common, Arbitrary, Priority, Sum protocols can be used

## Slide 49: Summary (Cont.)
Physical Complexity of an Ideal Parallel Computer
  Processors and memories are connected via switches
  Switches must operate in O(1) time at the level of words, for a system of p processors and m words, the switch complexity is O(mp)
  For meaningful values of p and m, a true PRAM is not realizable

## Slide 50: Summary (Cont.)
Communication Costs in Parallel Machines
Message Passing Costs in Parallel Computers
  Startup time, Per-hop time, Per-word transfer time
  Store-and-Forward Routing
  Packet Routing
  Cut-Through Routing
  Simplified Cost Model for Communicating Messages

## Slide 51: Additional Resources
Book: Introduction to Parallel Computing by Ananth Grama and Anshul Gupta
  Chapter 1: Introduction to Parallel Computing
    1.1 Motivating Parallelism
Flynn, M., “Some Computer Organizations and Their Effectiveness,” IEEE Transactions on Computers, Vol. C-21, No. 9, September 1972.
Kumar, V., Grama, A., Gupta, A., & Karypis, G. (1994). Introduction to parallel computing (Vol. 110). Redwood City, CA: Benjamin/Cummings.

## Slide 52: Questions?